## Slide 1: Dr. Eugen Martac, Fugro Germany Land
Newly Developed Aquifer Characterization Procedure
by Means of Hydraulic Profiling Tool and Mini Pump Tests
Batelle Palm Springs 2018
H3. High-Resolution Site Characterization (HRSC)

## Slide 2: Piping-Analysis based on hydraulic conductivity profiles
Estimation of effective K [K’]
Profiles of hydraulic conductivity
Piping modelling Model calibration to estimate K’-values
Application of K’
in Stability/Piping analysis
Dyke geotechnical remediation

## Slide 3: Piping-Stability analysis – case study
Hydraulic conductivity
regional databank K = 45 m/d
(pumping tests averaged over a 10km grid)
conservative estimation K = 17 m/d
(monitoring wells)
HPT/MPT effective K’ = 12 m/d
Important, since HTP/MPT method allows:
- +75% higher critical gradients (ic)
significant lower remediation requirement resp. need to invest

## Slide 4: State of the art…
Traditional derivation of hydraulic conductivities:
Empirical methods based on grain size distribution curves
Large scale modeling of aquifer behaviors
Slug-Tests or Pumping tests
Usually only as integral parameter, time and cost intensive derivation!
- Investigation of dyke stability through Cone Penetration Testing (cone resistence and lateral friction)
- Combined derivation of K and S values during CPT will offer significant time/costs advantages!

## Slide 5: State of the art...
Robertson et al., Can. Geotech. J. Vol. 29, 1992

## Slide 6: State of the art...
Dietrich et al, Ground Water, Vol. 46, #2, 2008.
DPIL = direct push injection log

## Slide 7: HPT – relative hydraulic conductivity
P* = Pmax – Patm – Phydro
Hydraulic Profiling Tool by GeopRObe
McCall & Christy 2010

## Slide 8: HPT/ST – absolute hydraulic conductivity
-Butler et al., Ground Water 2002
-Liu et al. Ground Water 2008
-Köber et al., Ground Water 2009
-Vienken Th., PhD Thesis, University of Tübingen 2010

## Slide 9: State of the art…
Batelle Chlorinated Hydrocarbons Conference Monterey 2012

## Slide 10: State of the art...
Control Plane 1
Control Plane 2
TCE
cisDCE
VC
CHC
174,4 g/d
0,5 g/d
136,5 g/d
36,9 g/d
12,1 g/d
0,0 g/d
10,7 g/d
0,0 g/d
Mass discharge
Spatial distribution of mass fluxes
Mass discharge = Σij (cij . Kij . Aij) . i
Hydraulic structuring
of the underground
Batelle Chlorinated Hydrocarbons Conference Monterey 2012

## Slide 11: Further development: MIP-HPT-CPT
Pump (CF)
Filter
HPT
Hydraulic Membrane
Wasser Injektion
Pressure transducer
HPT
MIP-CPT-HPT
HPT = Hydraulic
EC = Lithology + Salinity
MIP = Contamination
CPT = Lithology/Geotechnics
Dynamic pore water pressure
Notes: Möglichkeiten:
Hochauflösende Erfassung = Differenzierung der Kontamination zur Tiefe in Bezug zur Lithologie und Hydraulik.
Echtzeittechnologie = Adaptive Anpassung der Untersuchung = Kosteneffizienz.
Numerische Interpolation der digitalen Messdaten = 3-D Modelle.
Differenzierte Frachtenerfasung = optimierte Risikobewertung und Sanierung.
CPT-Daten und EC-Daten in Kombination lassen Bewertung von anaeroben CKW-Abbauvorgängen zu = Mineralisierung durch Chloridbildung.

## Slide 12: MIP-HPT-CPT für complicated sites
Glacial till identified only by friction ratio
Very important information from cone resistance and HPT
AquaConsoil CONFerence
barcelona 2013

## Slide 13: Further development: Power-HPT
Injection flowrate up to max. 5000 ml/min
Characterization of medium to high permeability horizons
Power-HPT
Aim: Hydraulic structuring of high permeability media Estimation of K-values from HPT logs?
Batelle Chlorinated Hydrocarbons Conference Monterey 2016

## Slide 14: Support method for civil/environmental engineering
AquaConsoil Copenhagen 2015
Application fields
Identification of dyke weak zones
Water modeling/management
Mass fluxes/mass discharge
Remediation scenarios, etc.

## Slide 15: Hydraulic characterization through HPT and MPT
AquaConsoil Copenhagen 2015
> 1 * 10-4
1 * 10-5 - 1 * 10-4
1 * 10-7 - 1 * 10-5
< 1 * 10-7
K-values(m/s)
Hydraulic characterization for identification of piping in dykes
mit
Φ = Water pressure
Q = Injection flowrate
R = Distance between Injektion port
and pressure transducer
Ks = Hydraulic (spherical) conductivity
Ss = Storage coefficient
t = Time since injection start
(Bruggemann, 1999)

## Slide 16: Hydraulic characterization: field deployment
HPT-MPT-CPT example
Left: u1 Pressure (red) and Injection flowrate (black), Right: inverse modeling of pressure/calibration of K-values
Aquifer with around 50m thickness
- 0 to 20 m bgl K-values between 10-30 m/d
- 20 to 50 m bgl K-values between 40-60 m/d

## Slide 17: Comparison of different derivation methods
Left: traditional physical derivation of hydraulic conductivity and MPT
Right: empirical derivation of hydraulic conductivity based on grain size distribution models. Large scale tests are displayed with vertical lines (red, blue and green).

## Slide 18: Scale effects of hydraulic conductivity derivation
Hydraulic conductivity versus Representative aquifer volume

## Slide 19
Proved system, high efficiency and appricability
R&D towards Channelling vs. Resolution degree
Support methodology for civil/environmental engineering
To remember:
HPT/MPT method allows a continuous appraisal of hydraulic conductivites during a traditional CPT push
Due to the monitored scale effects of the hydraulic conductivity derivation methods, the HPT/MPT is a much more appropiate method for large scale processes (like pipping) in comparison to small scale lab tests or Slug-Tests
Traditionally recorded geotechnical parameters (cone resistence and lateral friction) are not significantly influenced by the simultaneous use of the HPT/MPT-cone
HPT/MPT as efficient characterization method

## Slide 20
Proved system, high efficiency and appricability
R&D towards Channelling vs. Resolution degree
Support methodology for civil/environmental engineering
To remember:
HPT/MPT method allows a continuous appraisal of hydraulic conductivites during a traditional CPT push
Due to the monitored scale effects of the hydraulic conductivity derivation methods, the HPT/MPT is a much more appropiate method for large scale processes (like pipping) in comparison to small scale lab tests or Slug-Tests
Traditionally recorded geotechnical parameters (cone resistence and lateral friction) are not significantly influenced by the simultaneous use of the HPT/MPT-cone
e.martac@fugro.com
Thank you!
Questions ?